# Microphones

Sound is recorded by microphones which are transducers able to convert an acoustic signal into an electric one. There are three types of microphones:

- Pressure microphones which are sensitive to acoustic pressure

- Velocity microphones which are sensitive to particle velocity

- Hybrid microphones which are a combination of both quantities

A pressure microphone is completely omnidirectional, it receives sound from every direction. A velocity microphone is sensitive only to one of the three Cartesian components of the particle velocity vector, and hence presents a “figure of eight” directivity pattern, with reversed polarity when the sound comes form the “negative direction”.

Here a number of different microphone directivity patterns are shown. The first number is the percentage of sensitivity for pressure and the second for particle velocity.

# Cables

Cables are used to transmit the electric signal. A lot of signal contaminations can occur inside the cable. To solve this problem you need to use a balanced cable, with two wires carrying two identical copies of the signal with opposite polarity; the receiver records the difference between the voltage carried by the two cables, so that every noise or contamination isn’t recorded because is the same for each wire.

# Preamplifiers

The electric signal arrives to a preamplifiers which not only amplifies the signal but also processes it. The preamplifier can modify the frequency response, like an equalizer, but it can also add distortions to create a “better” musical sound.

# ADC (analog to digital converter)

There are two different types of ADC converters:

- PCM converters (like CD, DVD and DAT)

- Bitstream converters (DSD)

In the first type of converters the signal is represented by a series of integer numbers, with a number of bits between 16 and 24, and a sampling rate ranging between 44.1, 48, 96 or even 192 kHz.

In bitstream converters the sample frequency is much higher than PCM converters (typically 2.88 MHz) but there is a binary signal; each sample has just one bit: 1 or 0.

Bitstream converters are only employed within the Super Audio CD system.

# Techniques employed for sound recording and reproductions

# Mono followed by amplitude panning

This is a traditional method of recording and reproduction. The recording is mono; for example in an orchestra each musician has his microphone which records one track. Than all tracks are mixed with a surround panner so that it is possible to choose how to distribute the sound among the loudspeakers.

There are two types of panning:

- Pairwise panning where each signal is always sent to just two loudspeakers.

- Peter Craven panning where all the loudspeakers are always fed.

# ORTF Stereo

This technique is obtained using two microphones and two loudspeakers.

Each microphone feeds the corresponding loudspeakers. Microphones must be cardioid and they must be separated by a distance of 170-180 mm and they must create an angle of 110°. Than the best playback configuration is obtained when two loudspeakers and the listener form an equilateral triangle. The reproduction of sound is optimal only with this configuration.

# Binaural stereo dipole

This method provides an original two channels recording of the signal coming from N sources and the reproduction occurs over two loudspeakers which create with the listener an angle of 20°.

Sound is filtered by a digital system called cross talk canceller which can cancel the cross sound which leaves the right loudspeaker and arrives to the left ear and vice versa. To achieve this target it is possible to use a matrix with four filters and with some calculations each loudspeaker produces an additional sound, which cancels the cross sound of the opposite loudspeaker.

This system has some disadvantages like the difficulty to reproduce the low frequencies and the presence of a “sweet spot” which is the only one point where the reproduction is optimal.

It is possible also to create a dual stereo dipole placing two additional loudspeakers behind the listener, in order to reproduce the sound also in the rear hemisphere.

# Discrete microphone arrays ITU 5.1

This is an advanced technique with five microphones and five loudspeakers where each microphone feeds the corresponding loudspeaker.

Many different geometrical layouts exist, like

- Williams MMA

- INA−5

- OCT

- Etc…

These methods had a limited success mostly because of the little control during recording and during post processing and the technician’s work is very limited. It is also difficult to add to the recording tracks of separately recorded voices or instruments and also the fixed angle of covering cannot be adjusted after the recording is done.

# Ambisonic 3D

In this method the stage of capturing (or synthesizing) the signal is separated from the stage of reproduction.

For live recordings, a Soundfield™ microphone must be used, which captures a B−format 4−channels signal.

This particular signal is composed by four signals, W, X, Y, Z: W represents the omnidirectional pressure , whilst X, Y and Z represent the particle velocity in the three Cartesian directions.

The reproduction occurs over an array of 8−24 loudspeakers trough an Ambisonics decoder.

Today tetrahedral microphone arrays with four cardioid capsules are usually utilised, which can capture an A−format signal (the 4 “raw” capsule signals). This is then converted to the standard B−format signal by means of digital processing, usually performed by software.

In some cases, the B-format signal can be synthesized, starting from one or more mono sound tracks, which are “ambisonically-panned” by employing a software which “places” each soundtrack at user’s specified azimuth and elevation angles. This way of creating a synthetic B-format signal is usually called “encoding”.

At playback (usually called “decoding” in Ambisonics) the signal which is sent to each loudspeaker is a weighted mix of the four B−format channels, with weighting factors which only depends on the position of each loudspeaker; in fact these factors are the cosines of angles formed by loudspeakers with the three Cartesian directions.

It is also possible to add a small FIR filter for each loudspeaker, for matching perfectly the gain and phase of all loudspeakers.

The system shown in the following figure is a three-dimensional Ambisonics loudspeaker system, and the loudspeakers are placed on two squares, one vertical and one horizontal.

The signal decoding to feed the loudspeakers is done trough a DSP platform or with a computer. The DSP has four input channels and initially signals are split in high and low frequencies, because in the two cases different decoding coefficients are used, but then all signals are mixed together. Finally each speaker feed is equalised through an FIR filter.

# Hybrid method (Ambiophonics)

This technique combines an Ambisonics 3D system with a stereo dipole and merges the advantages and disadvantages of each method. For example the reproduction is optimal only in one point called “sweet spot” because of the presence of the stereo dipole but the entire system has a good surround effect due to the Ambisonics 3D system.

# Text boxes

Hybrid methods

Full ambisonics 3D

Discrete microphone array ITU 5.1

Binaural stereo dipole

Stereo ORTF

Mono followed by amplitude panning

ADC (analog to digital converter)

Preamplifiers

Cables

Type of microphones

TECHNIQUES EMPLOYED FOR SOUND RECORDING AND REPRODUCTION

INTRODUCTION