# Applied Acoustics  (Engineering) – 31/01/2014

Surname and Name:

Matricula:

1) The spectral analysis of the noise produced by a machine shows two strong peaks: 80+E dB(A) at 100 Hz and 70+F dB(A) at 2 kHz. Compute the total A-weighted sound pressure level in dB(A):

Ltot =                               dB(A)

2) In the same case of the previous exercise, compute the total unweighted sound pressure level in dB(LIN):

Ltot  =                                 dB

3) Find the distance travelled by a thunder in 3+E seconds when the air temperature is 10+F °C

d =		      	      m

4) A room is (5+D) meters long, (3+E) meters wide and (2+F) meters tall; all the surfaces are made of concrete, with an absorption coefficient 1 = 0.4 - F/30, except for the sound absorbing ceiling, which has an absorption coefficient 2 = 0.8 - E/30. Compute the reverberation time T20:

T20 = 			    s

5) Compute the critical distance in the previous room when the source has a directivity factor Q = 4+E :

dcr = 			      m

6) An infinitely long screen runs along a road, at a distance of  5+D/10 m from the center of  the runway.

The noise source is assumed as a line source at an elevation of 0.5m along the axis of the runway.

The noise screen is 3+E/10m tall, and the receiver is located at a distance of 50+F m from the screen and at an elevation of 4.0m. Compute the sound reduction caused by the screen at the frequency of 300 Hz.

L =			   dB

Note: each correct answer gives 5 points (tolerance: +/- 0.5 dB, +/- 5%).

Total score of exercises:

Oral examination:

# Text boxes

A

B

F

E

D

C

2+F

3+E

5+D

R

5+D/10 m

0.5 m

4 m

3+E/10 m

S

50+F m

TOTAL SCORE   Points: