# Applied Acoustics  (Engineering) – 28/02/2014

Surname and Name:

Matricula:

1) An alarm siren is rated to produce a sound pressure of 10+F Pa at a frequency of 1000*(1+E) Hz. Compute the unweighted sound pressure level in dB:

Lp =                              dB

2) In the same case of the previous exercise, compute the A-weighted sound pressure level in dB(A):

Lp,A  =                             dB(A)

3) A coastal surveillance station detects the explosion of a vessel. The acoustic impulse, detected by a microphone, travelling in air, arrives 10+F s later than the underwater acoustic impulse, detected by an hydrophone. Find the approximate distance of the explosion assuming standard values of c in air (340 m/s) and under water (1500 m/s).

d =		      	      m

4) A room is (5+D) meters long, (3+E) meters wide and (2+F) meters tall. A reverberation time T20 of 2+E/10 s is measured. Compute the average absorption coefficient  of the internal surfaces.



5) The reverberation time in the previous room is reduced to half, thanks to the insertion of 50+F*10 absorbing panels. Compute the equivalent absorption area of one panel.

A = 			   m2

6) An horn loudspeaker produces a sound pressure level of 100+D dB on axis, at a distance of 5+E m, and is rated with a directivity factor Q of 2+F. Compute its power level LW in dB.

LW =			   dB

Note: each correct answer gives 5 points (tolerance: +/- 0.5 dB, +/- 5%).

Total score of exercises:

Oral examination:

# Text boxes

A

B

F

E

D

C

d

5+D

2+F

3+E

TOTAL SCORE   Points: